## Slide 1: Assembly Language for Intel-Based Computers
Module 2
Processor Architecture
Slides prepared by Kip Irvine
Modified and supplemented by Clare Nguyen

## Slide 2: Overview: Processor Architecture
2
Since assembly programs work closely with hardware, it is important to have a basic understanding of
  How the CPU executes an assembly instruction
  How data is transferred and stored
The above are some of the factors that influence how an assembly program is written
Concepts covered in this section:
  Microprocessor Concepts
  Memory Management and Data Storage
  Input-Output System
(Read Chapter 2: 2.1- 2.3, 2.5)

## Slide 3: What's Next
3
Microprocessor Concepts
Memory Management and Data Storage
Input-Output System

## Slide 4: Basic Microcomputer Design
4
The central processor unit (CPU) has the following components:
The clock: synchronizes all CPU operations.
The control unit (CU): coordinates the sequence of execution steps.
The arithmetic and logic unit (ALU): performs integer arithmetic and bitwise operations.
The registers: store data temporarily during CPU operations.
The buses connect the CPU with other devices such as memory or IO:
The CPU uses the address bus to send out the address of the device it wants to access.
The CPU uses the control bus to send the control signal, such as read or write, to the appropriate device.
The data bus is used by the CPU and other devices to transport data to and from the CPU.

## Slide 5: Clock
5
There is one clock that runs at a constant rate.
The clock runs by cycling between a high and a low voltage, the high state is considered 1 and the low state is 0.
The transition from 0 to 1 is the rising edge, the transition from 1 to 0 is the falling edge.
One clock cycle is the time between a falling edge and the next falling edge.
The clock is used to trigger events: data is loaded onto the data bus at the beginning of a clock cycle, data is read into the CPU registers at a different clock cycle, etc.
All CPU and bus operations are synchronized to the clock cycle so they can work together in the right order and at the proper time.
The efficiency of an operation is measured in clock cycles: an instruction (operation) that takes 5 clock cycles to complete is considered faster than an instruction that takes 8 clock cycles to complete.

## Slide 6: CISC and RISC Architecture
For any processor, the number of clock cycles that an average instruction takes depends on whether the processor follows the CISC or RISC architecture.
CISC – complex instruction set computer (pronounced as “sisk”)
  Large instruction set with complex instructions.
  A complex instruction: high-level operation, made up of multiple steps.
  Requires a microcode interpreter to translate the instructions into hardware signals.
  Assembly programs use the complex instructions, which can do multiple tasks per instruction, so the programs tend to be shorter.
  The x86-based processors use a CISC architecture.
RISC – reduced instruction set computer (pronounced as “risk”)
  Small instruction set with simple instructions.
  A simple instruction: atomic instruction that does one basic step.
  Since the instructions are basic, they are directly executed by hardware.
  Assembly programs tend to be longer because the simple instructions need more coordination from the assembly program.
  The ARM processors use the RISC architecture. ARM is used in low-power, embedded applications such as hand-held game systems and cell phones.

## Slide 7: Instruction Execution (1 of 2)
7
Instruction Fetch: the CU fetches the instruction from the instruction queue into the instruction register, and increments the PC so it points to the next instruction
Instruction Decode: the CU decodes the instruction in the instruction register, and determines what operation needs to be performed by the ALU
Operand Fetch: if an operand (data) is in memory, the CU reads or fetches the operand and stores the data in internal registers. If the operand is already in a register, then this operand fetch step is not necessary.
Execute: the ALU performs the operation, using operands in the registers
Store output: if the output needs to be written to memory, the CU writes data to memory in this step. If the output is stored in a register, then this step is not necessary.
When a program runs, it is first loaded into memory and the first instructions are stored in an instruction queue [labeled I1, I2, I3, I4 in the diagram]
The program counter (PC) points to the next instruction to be run
For each instruction that runs, the control unit (CU) coordinates the following steps, 2 of which are optional:

## Slide 8: Instruction Execution (2 of 2)
8
Out of the 5 steps of an instruction execution:
  3 are always run: instruction fetch, instruction decode, execution
  2 are optional: operand fetch, store output
Running 3 steps means a faster execution time than running all 5 steps, so assembly programmers can optimize their programs by writing instructions such that execution takes 3 steps instead of 4 or 5
This can be done by storing data in registers instead of in memory whenever possible
In addition to the programmer optimized code, a program also runs faster due to advances in the CPU architecture, shown in the next slides

## Slide 9: Non-Pipelined Instruction Execution
9
The first processors used non-pipelined instruction execution.
Non-pipelined execution means each instruction is run one at a time: when an instruction is finished then the next instruction will run.
Since each instruction can take up to 5 steps to finish, running each instruction in non-pipelined mode results in wasted clock cycle.
The CPU has to wait for the instruction and data fetches, and sits idle during most of the instruction execution.
Example of a non-pipelined processor: Instruction I1 takes 6 clock cycles, then instruction I2 runs, taking another 6 clock cycles. The 2 instructions take up 12 clock cycles when running in non-pipelined mode.

## Slide 10: Pipelined Instruction Execution
10
Pipelining makes it possible for the processor to execute instructions more in parallel.
Instruction execution is divided into discrete stages: at each clock cycle, different instructions can be at different stages. This makes it possible to process several instructions at a time.
Using the same example with 2 instructions I1 and I2, it now only takes 7 clock cycles for the 2 instructions to finish. For example, in clock cycle 1: I1 is fetched. In clock cycle 2: I1 is decoded and I2 is fetched. In clock cycle 3, I1 operands are fetched while I2 is being decoded, etc.
Pipelining results in more efficient use of clock cycles by the CPU, therefore producing greater throughput of instructions.
For k stages and n instructions, the number of required cycles is:
k + (n – 1)

## Slide 11: Wasted Cycles in Pipelining
11
Even with pipelining, when one of the stages requires two or more clock cycles, clock cycles are again wasted.
In the example below, in stage S4, instruction I1 requires 2 cycles to finish, so instruction I2 has to wait in stage S4 for 2 clock cycles before it can get to stage S5.
For k stages and n instructions, where one stage requires 2 clock cycles, the number of required cycles is:
k + (2n – 1)

## Slide 12: Multicore
12
A multicore processor has multiple execution pipelines and multiple execution units.
In the following example, stage S4 takes 2 clock cycles to finish, so it is built with left and right pipelines (u and v).
Instruction I1 enters the u pipeline into stage 4, it stays in stage S4 for 2 clock cycles as before, and is processed by one execution unit. Instruction I2 doesn’t have to wait an extra clock cycle to enter stage S4, it can enter stage S4 in the next cycle by using the v pipeline and gets processed by a different execution unit.
Newer processors now all run in multicore mode.
For k stages and n instructions, the number of required cycles is:
k + n

## Slide 13: Reading from Memory (1 of 2)
13
Why do some instructions take more clock cycles to execute than others?
In a CISC processor, some instructions handle complex tasks that have multiple microcode steps. These instructions will take more clock cycles than simpler instructions.
Some instructions require the operand fetch or the store output optional steps. Fetching data from memory or storing data to memory always require multiple clock cycles.
Conventional memory is RAM (random access memory).
Even though RAM is getting faster all the time, it is still slow compared to registers that reside right on the CPU chip.
Memory also responds much more slowly than the CPU due to the synchronization between memory and CPU.

## Slide 14: Reading from Memory (2 of 2)
14
The steps that the CPU takes to read data from memory, such as in the operand fetch step:
  The CPU places the memory address on the address bus (cycle 1).
  The CPU sets the Read Line (RD) to 0, indicating that data is being requested from memory (cycle 2).
  The CPU waits one clock cycle for the memory at the requested address to respond (cycle 3).
  The Read Line (RD) goes to 1, indicating that the data is available on the data bus (cycle 4).
  Data is read in by the CPU from the data bus (cycle 5).

## Slide 15: Cache Memory
15
What is cache memory?
High-speed but expensive static RAM both within and outside the CPU chip.
- Level-1 cache: on the CPU chip.
- Level-2 cache: outside the CPU chip.
Why use cache?
- Because conventional memory in RAM is much slower than the CPU, the most recently used data are stored in cache memory for faster access.
- The idea is that the most recently used data will more likely be needed again within the next instructions, and if they are in cache, they can be fetched back faster.
- The use of cache is determined by the hardware in the CPU, the programmer has no control over whether data is stored in convention memory or cache.
How well does cache improve access to data?
- In general, a large cache will have noticeable effect on data access time.
- Cache hit: when data to be read is already in cache memory, this is the ideal situation.
- Cache miss: when data to be read is not in cache memory, in this case data has to be fetched from conventional memory and then stored in cache.

## Slide 16: Multitasking (1 of 2)
16
The OS appears to run multiple tasks at the same time
  A task can be a process or a thread of execution.
  A process has its own memory space and can have multiple threads. A program running in memory is a process.
  A thread shares its memory with other threads in the same process. A thread in a program can be used to display graphics, while another thread in the same program is for reading user input.
  For multitasking to occur:
    The OS must have a scheduler.
    The processor must support task switching.
The job of a scheduler:
  Since the CPU can only run one instruction at a time, the scheduler allocates a given amount of the CPU time to each task. The rapid switching of tasks gives the illusion that all programs are running at the same time.
  The scheduler generally uses a round robin approach: each task gets its turn with the CPU for a certain amount of time, and all tasks are serviced by the CPU before the CPU will repeat running the first task.
  The OS also assigns a priority number to each task, and the higher priority level task can interrupt (or cut in front of) a lower priority task in the round robin.

## Slide 17: Multitasking (2 of 2)
17
Task switching by the processor:
  Each time the processor needs to switch to another task, it saves the state of the current task
  When it switches to the next task, the processor fetches the saved state of this next task. This way the processor can have the correct data, the correct status flags, and the correct instructions in order to continue with this task.

## Slide 18: What's Next
18
Microprocessor Concepts
Memory Management and Data Storage
Input-Output System

## Slide 19: Modes of Operation
19
Common modes for the X86 based processors
Real address mode:
  Native mode of MS-DOS operating system.
  Each program can have direct access to any part of system memory. In this mode a user program can crash the system if there is error accessing system memory.
Protected mode:
  Native mode of Windows and Linux operating systems.
  Each program is given separate memory segments to run and use, and the processor prevents user programs from accessing memory outside the assigned segments (this is what’s known as a ‘segmentation fault’).
  This mode is safer than the real address mode because user programs generally cannot crash the system.
  Programs in this class will be using this mode.
Virtual-8086 mode
  Hybrid of protected mode and real address mode.
  The memory is set up such that each program has its own virtual processor and can access any part of the virtual system memory.

## Slide 20: Memory Allocation
20
Based on the processor mode, the OS allocates a certain memory
block size and memory addressing scheme for each program that runs.
Currently we use the 32-bit processing, which means:
In protected mode
  - 4 GB: size of memory block that the program can use.
  - 32-bit address: each memory address is 32 bit long, to address 232 or 4 GB of memory.
  - For this class we will write programs in this mode.
In real address and virtual-8086 modes
  - 1 MB: size of memory block that the program can use.
  - 20-bit address: each memory address is 20 bit long, to address 1MB of memory.

## Slide 21: Memory Allocation in Protected Mode
21
Each program is assigned a memory partition which is protected from other programs. User programs cannot access system memory and are less likely to crash the system when there is error accessing memory.
4 GB addressable RAM, with address range of 0 to FFFF FFFF, which is 232 .
The OS keeps track of memory allocated to each program in segment descriptor tables.
Program memory allocation:
  Each program is allocated 3 memory segments for code, data, and the run time stack.
  The address of the code segment, data segment, and stack segment belong in the descriptor table.
Two memory models are used in protected mode:
  flat segment model: each program has access to the entire 4GB of addressable memory
  multi segment model: each program has part of the addressable memory.
MASM programs use the flat memory model. This is the memory model we use for the class.

## Slide 22: Flat Memory Model
22
There is one global descriptor table (GDT) for the system, which has many segment descriptors.
Each segment descriptor is for a code segment, data segment, or stack segment.
The segments used by each program (code, data, stack) together use the entire 32-bit addressable space (4GB) of memory.
A program needs to have at least a code segment and a data segment. The stack segment is optional.
Large programs can use multiple code and data segments.

## Slide 23: Virtual Memory and Paging
23
Each memory segment is divided into 4096-byte (4K) blocks called pages, and the coordination of all the different pages so they are seamless to the program is called paging.
Paging allows the total memory used to be larger than physical memory (we don’t have to have 4GB of RAM on our computers, yet we have 4GB of addressable memory to use for our program).
Part of total memory used by a program is in memory, the rest is on disk.
The total amount of memory used, both in memory and on disk, is called virtual memory.
The virtual memory manager (VMM) is an OS utility that manages the loading and unloading of pages (called swapping).
Paging is supported directly by the CPU, the programmer does not control the paging or swapping of memory.
A page fault is issued by the CPU when a page must be loaded from disk. When a page fault occur, performance is slower.
The larger the physical memory, the less page fault will occur.

## Slide 24: Named Registers (1 of 2)
24
Assembly programs have 2 places to store data that it uses:
  Variables in memory (data segment) of the program
  Named registers
Named registers are special data storage locations inside the CPU.
They are called named registers because the programmer accesses them by specific names.
They are optimized for speed and provide faster access to data than memory.
However, they can only be used by an instruction for temporary data storage since there is a small number of them.
Some registers can be used by any instruction, and some registers are only used for certain purpose.
Some instructions work only with a certain register.
Unlike HLL programming, where all data are stored in variables, in assembly programming we have a choice: store data in variables (in memory) or store data in named registers.

## Slide 25: Named Registers (2 of 2)
25
The named registers are:
4 32-bit general purpose registers): EAX, EBX, ECX, EDX
4 32-bit base and index registers, which can also be used for general purpose: EBP, ESP, ESI, EDI
1 32-bit flag register: EFLAGS
1 32-bit instruction pointer register: EIP
6 16-bit segment registers: CS, DS, SS, ES, FS, GS

## Slide 26: Accessing General Purpose Registers
26
For the general purpose registers EAX, EBX, ECX, EDX:
Each register can be accessed by using its 8-bit name, 16-bit name, or 32-bit name.
Two different 8-bit names will access the lower 8 LSBs or the higher 8 LSBs of the register: AL and AH.
A 16-bit name will access the LSB half of the register: AX
A 32-bit name will access the entire register: EAX
By using the correct name of a general purpose registers, the programmer can access a part of the register

## Slide 27: Accessing Other Registers
27
For the base and index registers ESI, EDI, EBP, ESP:
A 16-bit name SI or DI will access the LSB half of the register.
A 32-bit name ESI or EDI will access the entire register.
For the instruction pointer register EIP:
A 16-bit name IP will access the LSB half of the register
A 32-bit name EIP will access the entire register

## Slide 28: Some Specialized Register Uses (1 of 2)
28
There are some specialized uses for each register. The basic explanation is given here and the details will be covered in later chapters when these registers are being used with certain instructions.
General purpose registers:
  EAX – accumulator*: computation instructions typically use EAX to store the output.
  EBX – base offset*: used for indirect addressing of memory.
  ECX – loop counter*: used by looping instructions.
  EDX – multiplication and division*: used for multiply and divide operations.
Base and index registers:
  ESP – stack pointer*: points to the stack top of the run time stack.
  ESI, EDI – source and destination index registers*: for indirect addressing and array indexing.
  EBP – stack frame base pointer*: used in procedure call.
*The E (in the name of some registers) is for extended: 32 bits instead of 16 bits

## Slide 29: Some Specialized Register Uses (2 of 2)
29
Segment registers:
  CS – code segment: points to where code (instructions) are in memory.
  DS – data segment: points to where data are in memory.
  SS – stack segment: points to where the stack is in memory.
  ES, FS, GS - additional segments: for when the program needs more memory segments.
Instruction pointer register:
  EIP – instruction pointer*: points to next instruction that is going to be executed. Each time an instruction is fetched at the start of an instruction cycle, EIP increments so that it can point to the next instruction.
Flag register:
  EFLAGS : maintains states of status and control flags
  each flag is one bit of the register
*The E (in the name of some registers) is for extended: 32 bit, instead of 16 bits

## Slide 30: Status Flags
30
Flags are commonly used for conditional branching in a program, such as with if statements or loops.
Each bit in the flag register EFLAGS represents one flag:
    1 means the bit is set
    0 means the bit is clear (not set)
Some commonly used flags:
Flag names Set under these conditions
Carry unsigned arithmetic out of range
Overflow signed arithmetic out of range
Sign result is negative
Zero result is zero

## Slide 31: Data in Registers
The name of each register dictates the size (how many bits) of data that is stored in the register.
If the decimal value 12 is stored in the AH register:
the hexadecimal value in AH: 0C
If the decimal value -2 is stored in the CX register:
the hexadecimal value in CX: FFFE
the hexadecimal value in CH: FF
the hexadecimal value in CL: FE
If the decimal value 18 is stored in the EDX register:
the hexadecimal value in EDX: 0000 0012
the hexadecimal value in DX: 0012
the hexadecimal value in DH: 00
the hexadecimal value in DL: 12
If the character ‘A’ is stored in the AL register:
the hexadecimal value in AL: 41
Note that the data in registers are always in binary (or hexadecimal for shorter representation), regardless of whether the data is a signed or unsigned number or even a character.

## Slide 32: Data in Memory (1 of 2)
Here is an example of what data looks like when we use a debugger to see a part of memory used by the program:
The displayed addresses start at 00405000 and increments by 1.
Each address is for 1 byte of data, the smallest addressable unit of memory.
Each line of data above has 12 bytes of data: data 48 is at address 00405000, data 65 is at 00405001, data 6c is at 00405002…
Starting at address 00405000 to 0040500A, the bytes 48, 65, 6c, 6c, 6f … are the hexadecimal data that, when converted to ascii characters, make up the string “Hello world” (shown on the right side column).
Without using hexadecimal, the string “Hello” in binary would look like:
0100 1000 0110 0101 0110 1101 0110 1101 0110 1111
This part of memory begins at address 00405000
addresses
data
ascii equivalence
The data value 6c is stored at address 00405009
The data value 48 is stored at address 00405000

## Slide 33: Data in Memory (2 of 2)
Data are stored as bytes (2 hexadecimal digits) in memory.
An 8-bit data value takes up 1 byte, such as the letter ‘H’ below with the hexadecimal value 48, at address 00405000.
A word or 16-bit data takes up 2 bytes, a doubleword or 32-bit data value takes up 4 bytes of memory.
This part of memory begins at address 00405000
addresses
data
ascii equivalence
The data value 6c is stored at address 00405009
The data value 48 is stored at address 00405000

## Slide 34: What's Next
34
Microprocessor Concepts
IA-32 Memory Management and Data Storage
Input-Output System

## Slide 35: Levels of Input Output (1 of 2)
35
The IO of a system is available for use at different levels of software
Level 3: A library function
  Generic text or file I/O
  Easy to code, details are hidden
  Slowest performance
Level 2: An operating system function
  From an API library, such as functions to display graphics
  Specific to one OS but device independent
  Medium performance
Level 1: A BIOS (basic input-output system) function
  Low level routines that control hardware devices, such as control of color or sound
  May produce different results on different systems
  Knowledge of hardware required
  Usually good performance
Level 0: Communicate directly with the hardware
  May not be allowed by some operating systems
  Sends and receives data at specific ports

## Slide 36
36
When a program displays a string of characters, the following steps take place:
Level 3: The string output statement in the program runs, calling OS functions.
Level 2: The OS functions receive the string pointer and call BIOS functions in a loop to process each character.
Level 1: The BIOS functions map each character to the right size, font, color… and send data to a hardware port.
Level 0: The port is connected to a video controller card, which generates signals at the right time to display the character in pixels.
Unlike a HLL program that only works at Level 3, an assembly program can perform input-output at level 1, or can call the OS functions directly.
Levels of Input Output (2 of 2)

## Slide 37: Summary of Key Concepts
37
Since assembly programs work closely with hardware, it is important to know the basic architecture of the system.
Each instruction in an assembly program is run in an instruction cycle, which involves coordination between the CPU and other devices, such as memory.
Memory access is slow compared to CPU execution time, so the system architecture makes up for this by using: registers, cache, pipelining and multicore processing.
In the Intel CPU family, the CPU we use and the OS we use dictate what modes we can run, and the mode determines how the OS sets up memory for our program.
Given a memory set up, we can choose which memory model to use, and the memory model dictates how much memory is allocated for our program.
When our program accesses memory, there is paging involved.
The register name determines the size of data that is accessed.
Data are stored as consecutive bytes in memory, and each byte of memory has a specific address.
The CPU works with different IO devices through ports. Assembly allows us to work with IO ports at a lower level than a HLL.