## Slide 1: Assembly Language for Intel-Based Computers
Module 4
Data Transfer
Integer Arithmetic
(c) Pearson Education, 2012. All rights reserved.
Slides prepared by Kip Irvine
Modified and supplemented by Clare Nguyen

## Slide 2: Overview: Data Transfer
2
It is important to be able to move data from one location to another when a program runs:
  When the CPU works on data, typically the input data and the resulting data are in registers. Therefore data need to be moved into registers before the operation, and data may need to be moved out of a register after the operation.
  Some instructions work only with certain registers, so data need to be in the correct registers before the operation.
In addition, the data can be accessed directly or indirectly through an address.
Concepts covered in this section:
  Data Transfer Instructions
  Direct Memory Access
(Read Chapter 4: 4.1)

## Slide 3: What’s next
Data Transfer Instructions
Direct Memory Access

## Slide 4: Operand Types
Three basic types of operands are used by assembly instructions:
Immediate – a literal integer (8, 16, or 32 bits).
  The constant value is encoded within the machine instruction by the assembler (so the value can be found immediately, thus the name).
  Example: mov ax, 10 ; 10 is an immediate operand
Register – the name of a register.
  The assembler converts the register name to a number and encode it within the machine instruction.
  During execution, since the register is on the same chip as the CPU, there is no data fetching cycle necessary. This makes registers a much more efficient temporary data storage than memory.
  Example: inc bx ; bx is the register operand
Memory – reference to a location in memory.
  Recall that a variable name is actually a label in the data segment, which means it refers to a memory address where the data is stored.
  The address is encoded within the machine instruction by the assembler.
  For direct addressing, the data is stored in memory, at the given address.
  For indirect addressing, a register holds the address of the memory location, so the address in the register will have to be dereferenced to access data.
  During execution data will need to be fetched from or written to memory, resulting in one extra step in the instruction cycle.
  Example: mov al, value ; where value is a defined as value byte 10

## Slide 5: MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count ; bl = 100
mov ax,wVal ; ax = 2
mov count,al ; count = 2
mov al,wVal ; error, operand size mismatch
mov wVal,count ; error, 2 memory operands
The most common data transfer instruction is MOV
MOV moves data from source to destination.
Syntax: MOV destination, source
Rules for destination and source operands:
  Destination and source must be the same size (there is no implicit conversion of data type by the assembler, unlike with a compiler).
  Destination cannot be an immediate (obvious reason).
  Only one memory operand is permitted (memory access is too long for two memory fetches).
  CS, EIP, and IP cannot be the destination (the OS wants to be in charge of the code segment and the instruction queue).
  Cannot move immediate to any segment register.

## Slide 6: Your turn . . .
.data
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.code
mov ds,45
mov esi,wVal
mov eip,dVal
mov 25,bVal
mov bVal2,bVal
Explain why each of the following MOV statements are invalid:
immediate move to DS not permitted
size mismatch
EIP cannot be the destination
immediate value cannot be destination
memory-to-memory move not permitted

## Slide 7: Zero Extension
mov bl,10001111b ; 8-bit value
movzx ax,bl ; zero-extend to 16 bits
movzx ecx,bl ; zero-extend to 32 bits
MOV requires that source and destination operands are the same size
But sometime you want to copy the source data to a larger size destination register.
MOVZX instruction copies the source data into a 16 or 32 bit register and fills (extends) the upper half of the destination with zeros.
MOVZX is for move with zero extension.
MOVZX should only be used for unsigned integers (why?)
The destination operand must be a register.

## Slide 8: Sign Extension
mov bl,10001111b ; bl = 8fh
movsx ax,bl ; ax = ff8fh
mov bl,01001111b ; bl = 4fh
movsx ax,bl ; ax = 004fh
For signed integers, use MOVSX to copy a source data to a larger size 16 or 32 bit register.
MOVSX fills the upper half of the destination with a copy of the source operand's sign bit, which may be 0 or 1.
MOVSX is for move with sign extension.
The destination operand must be a register.

## Slide 9: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
xchg ax,bx ; exchange 16-bit regs
xchg ah,al ; exchange 8-bit regs
xchg var1,bx ; exchange mem, reg
xchg eax,ebx ; exchange 32-bit regs
xchg var1,var2 ; error: two memory operands
XCHG exchanges (swaps) the values of two operands.
At least one operand must be a register.
The operands must be the same size.
No immediate operands are permitted.
XCHG is faster than using 3 MOV instructions.

## Slide 10: What’s next
Data Transfer Instructions
Direct Memory Access

## Slide 11: Direct Memory Operands
A direct memory operand is a variable name that refers to an address in memory.
In the example below, var1 is a direct memory operand of the mov instruction. It is the label (or name) of a memory location that is initialized to 10h.
The variable name is automatically dereferenced by the assembler.
In the example below, var1 or [var1] means the same: data will be fetched from the memory location labeled var1.
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
alternate format (rarely used for direct memory operands since no one wants to do extra typing)

## Slide 12: Direct-Offset Operands (1 of 2)
.data
arrayB BYTE 10h,20h,30h,40h
.code
mov al,arrayB ; AL = 10h
mov al,arrayB + 0 ; same thing
mov al,arrayB + 1 ; AL = 20h
mov al,[arrayB + 1] ; alternative notation
mov al,arrayB + 3 ; AL = 40h
Direct offset operands are used to access an array.
A constant offset is added to the array name to produce an effective address.
The offset is the number of bytes away from the beginning of the
array.
The effective address is then used to access the value at the memory location.

## Slide 13: Direct-Offset Operands (2 of 2)
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax,arrayW + 2 ; AX = 2000h
mov ax,arrayW + 4 ; AX = 3000h
mov eax,arrayD + 4 ; EAX = 00000002h
In the previous example, incrementing by 1 means go to the next byte of data in arrayB, which means go to the next element, since arrayB is an array of bytes.
If an array contains words, incrementing by 2 will access consecutive
words of data, or access consecutive elements.
Likewise, if an array contains doublewords, incrementing by 4 will access consecutive doublewords of data or consecutive elements.
When we add a constant value to an array name, we are adding the number of byte offsets from the first memory location that the array occupies.

## Slide 14: Example (1 of 2)
Write instructions that rearrange the values of three doubleword values in the following array so they are in the order: 3, 1, 2.
  .data
  arrayD DWORD 1,2,3
Step 2: Exchange EAX with the third array value and copy the value in EAX to the first array position.
Step1: copy the first value into EAX and exchange it with the value in the second position.
mov eax,arrayD
xchg eax,arrayD + 4
xchg eax,arrayD + 8
mov arrayD,eax

## Slide 15: Example (2 of 2)
To add the following unsigned bytes together:
.data
myBytes BYTE 80h,66h,0A5h
Will the following code work?
mov al, myBytes
add al,myBytes+1
add al,myBytes+2
Will the following code work?
mov ax, myBytes
add ax,myBytes+1
add ax,myBytes+2
How about the following code?
movzx ax,myBytes
mov bl,myBytes+1
add ax,bx
mov bl,myBytes+2
add ax,bx
Yes
No. myBytes is a different size (byte) than ax (word)
Yes, but…
… to be safe, need to zero out the upper byte of bx before adding bx to ax

## Slide 16: Summary of Key Concepts
16
When moving data from or to a register or memory location, there must be a match between the size of the data and the size of the storage location.
If the size of the storage location is larger than the size of the data value, use the MOVZX for unsigned data and MOVSX for signed data.
When swapping data between memory locations, XCHG takes less coding than MOV.
When accessing arrays with [arrayname + n], n represents the number of byte offsets.

## Slide 17: Overview: Integer Arithmetic
17
When doing integer arithmetic, assembly programmers have two extra considerations compared to a HLL programmer:
  Status Flags
  Instructions that require specific registers
Concepts covered in this section:
  Addition and subtraction
  Flags in addition and subtraction
  Unsigned multiplication and division
  Signed multiplication and division
(Read Chapter 4: 4.2, Chapter 7: 7.4 )

## Slide 18: What's Next
Addition and subtraction
Status flags in addition and subtraction
Unsigned multiplication and division
Signed multiplication and division

## Slide 19: INC and DEC Instructions
INC increments the value of its operand.
DEC decrements the value of its operand.
It is more efficient to use INC rather than ADD to add 1 to an operand.
It is also more efficient to use DEC rather than SUB to subtract 1 from an operand.
DEC and INC uses only one operand. The operand may be a register or memory.
Syntax: INC destination
    Logic: destination  destination + 1
Syntax: DEC destination
    Logic: destination  destination – 1

## Slide 20: INC and DEC Examples
.data
myWord WORD 1000h
myDword DWORD 10000000h
.code
inc myWord ; 1001h
dec myWord ; 1000h
inc myDword ; 10000001h
mov ax,00FFh
inc ax ; AX = 0100h
mov ax,00FFh
inc al ; AX = 0000h

## Slide 21: Exercise
Show the value of the destination operand after each of the following instructions executes:
.data
myByte BYTE 0FFh, 0
.code
mov al,myByte ; AL =
mov ah,[myByte+1] ; AH =
dec ah ; AH =
inc al ; AL =
dec ah ; AX =
FFh
00h
FFh
00h
FE00

## Slide 22: ADD and SUB Instructions
Syntax: ADD destination, source
  Logic: destination  destination + source
Syntax: SUB destination, source
  Logic: destination  destination – source
Same operand rules as for the MOV instruction:
  Destination and source must be the same size.
  Destination cannot be an immediate.
  Only one memory operand is permitted.
  EIP, IP, and segment registers cannot be the destination.

## Slide 23: ADD and SUB Examples
.data
var1 DWORD 10000h
var2 DWORD 20000h
.code ; ---EAX---
mov eax,var1 ; 00010000h
add eax,var2 ; 00030000h
add ax,0FFFFh ; 0003FFFFh
add eax,1 ; 00040000h
sub ax,1 ; 0004FFFFh

## Slide 24: NEG Instruction
.data
valB SBYTE -1
valW SWORD +32767
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32767
Negates an operand or reverses the sign of an operand.
Operand can be a register or memory operand.
Suppose AX contains –32,768 and we apply NEG to it. Will the result be valid?
No, AX cannot store the value +32,768 because it is larger than a signed word. To determine if a value is valid or not, after the negation you would need to check the status flag to see if an overflow occurs. Status flags are covered later in this module.

## Slide 25: NEG Instruction and the Flags
.data
valB BYTE 1,0
valC SBYTE -128
.code
neg valB ; CF = 1
neg [valB + 1] ; CF = 0
neg valC ; CF = 1
The processor implements NEG by using the following internal operation:
SUB 0,operand
Any nonzero operand causes the Carry flag to be set.

## Slide 26: Implementing Arithmetic Expressions
.data
Rval DWORD ?
Xval DWORD 26
Yval DWORD 30
Zval DWORD 40
.code
mov eax,Xval
neg eax ; EAX = -26
mov ebx,Yval
sub ebx,Zval ; EBX = -10
add eax,ebx
mov Rval,eax ; Rval = -36
HLL compilers translate mathematical expressions into assembly instructions.
You, too, can be a “compiler” and turn a HLL mathematical expression into assembly instructions.
For example:
Rval = -Xval + (Yval – Zval)
can be translated to:

## Slide 27: Example
mov ebx,Yval
neg ebx
add ebx,Zval
mov eax,Xval
sub eax,ebx
mov Rval,eax
Translate the following expression into assembly language.
Rval = Xval - (-Yval + Zval)
- Assume that all values have been defined as signed doublewords.
Use the same variable names.
Do not permit Xval, Yval, or Zval to be modified:

## Slide 28: What's Next
Addition and subtraction
Status flags in addition and subtraction
Unsigned multiplication and division
Signed multiplication and division

## Slide 29: Flags Affected by Arithmetic
The ALU has a number of status flags that reflect the outcome of arithmetic and bitwise operations:
  The flags are set or cleared based on the result stored in the destination operand.
  Set is 1, clear is 0.
Commonly used flags:
  Zero flag – set when destination equals zero
  Sign flag – set when destination is negative
  Carry flag – set when unsigned value is out of range
  Overflow flag – set when signed value is out of range
The MOV instruction never affects the flags.

## Slide 30: Concept Diagram
status flags
ALU
conditional jumps
branching logic
arithmetic & bitwise operations
part of
used by
provide
attached to
affect
CPU
This diagram shows the role of the status flags in an assembly program.
Note that each time the ALU performs an arithmetic or bitwise operation, the status flags could change state.
executes
executes

## Slide 31: Zero Flag (ZF)
mov cx,1
sub cx,1 ; CX = 0, ZF = 1
mov ax,0FFFFh
inc ax ; AX = 0, ZF = 1
inc ax ; AX = 1, ZF = 0
The Zero flag is set when the result of an operation produces zero in the destination operand.

## Slide 32: Sign Flag (SF)
mov cx,0
dec cx ; CX = -1, SF = 1
add cx,2 ; CX = 1, SF = 0
The Sign flag is set when the destination operand has a negative result. The flag is clear when the destination operand has a positive result.
The sign flag is a copy of the destination's MSB:
mov al,0
dec al ; AL = 11111111b, SF = 1
add al,2 ; AL = 00000001b, SF = 0

## Slide 33: Signed and Unsigned Integers
All CPU instructions operate exactly the same way for both signed and unsigned integers, because the ALU does not distinguish between signed and unsigned integers (a data value is just 1’s and 0’s to the hardware).
  Example:
    mov ax, e000h
    add ax, 1fffh ; ax = ffffh, SF = 1
YOU, the programmer, are responsible for using the correct data type and interpreting the result based on the correct data type.
In the example above, after the 2nd instruction runs, SF is 1. Is the value of SF important?
  No: If you are working with unsigned integers, then ax contains the value 65,535 decimal, and you don’t need to look at the SF value.
  Yes: If you are working with signed integers, then ax contains the value -1 decimal. You need to check SF if you want to catch negative values.

## Slide 34: OF and CF – Hardware Viewpoint (1 of 2)
Ultimately all instructions are executed by the logic of the hardware (level 0), so first we need to understand how the OF (overflow flag) and CF (carry flag) get set by the CPU.
Recall that XOR (eXclusive OR) is a Boolean operation with 2 input:
  a XOR b = 0 if a and b are both 1 or both 0
  a XOR b = 1 if a=1, b=0 or a=0, b=1
How the ADD instruction modifies OF and CF in hardware:
  OF = (carry out of the MSB) XOR (carry into the MSB)
  CF = carry out of the MSB
  1100 0000
  +0100 0000
  (1) 0000 0000 CF = 1 because there is carry out from the MSB
  OF = 0 because there is carry out of MSB and
  carry in to MSB
  0100 0000
  +0100 0000
  (0) 1000 0000 CF = 0 because there is no carry out from the MSB
  OF = 1 because there is no carry out of MSB but there
  is carry in to MSB

## Slide 35: OF and CF – Hardware Viewpoint (2 of 2)
How the SUB (subtraction) instruction modifies OF and CF in hardware:
  Subtraction means to negate the source operand (using 2’s complement) and add it to the destination.
  OF = (carry out of the MSB) XOR (carry into the MSB)
  CF = borrow for the MSB
  CF value is the reverse of the carry out value (1 to 0, or 0 to 1)
  Example
  0111 1111 0111 1111
  - 1000 0001  + 0111 1111 (2’s complement)
  1111 1110
  CF = 1 because there is no carry out (carry out is 0)
  OF = 1 because there is no carry out of MSB but there is carry in to MSB

## Slide 36: Carry Flag (CF)
When CF is set, it means the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).
Therefore when working with unsigned integers, it is a good idea to check CF to determine if the result is valid or not. If CF is set, the result is invalid.
For unsigned integers:
mov al,0FFh ; AL = 255
add al,1 ; CF = 1, AL = 0
; invalid result
; Try to go below zero:
mov al,0 ; AL = 0
sub al,1 ; CF = 1, AL = 255
; invalid result

## Slide 37: Example
mov ax,00FFh
inc ax ; AX= SF= ZF= CF=
dec ax ; AX= SF= ZF= CF=
inc al ; AL= SF= ZF= CF=
mov bh,6Ch
add bh,95h ; BH= SF= ZF= CF=
mov al,2
sub al,3 ; AL= SF= ZF= CF=
For each of the following marked entries, show the values of the destination operand and the Sign, Zero, and Carry flags:
0100h 0 0 0
00FFh 0 0 0
00h 0 1 1
01h 0 0 1
FFh 1 0 1

## Slide 38: Overflow Flag (OF)
When OF is set it means the signed result of an operation is invalid or out of range.
When working with signed integers, it is a good idea to check OF to determine if the results of arithmetic operations are valid.
For signed integers:
mov al,+127 ; AL = 7Fh
inc al ; OF = 1, AL = 80h = -128,
; invalid result for signed integers

## Slide 39: Tips for Evaluating OF
mov ax,8000h
add ax,2 ; CF = OF =
mov ax,0
sub ax,2 ; CF = OF =
mov al,-5
sub al,+125 ; OF =
When adding 2 integers, think of them as signed integers (regardless of whether they are actually signed or unsigned):
  When one integer is positive and the other is negative, OF is never set.
  When both integers are positive and the result is negative, OF is set.
  When both integers are negative and the result is positive, OF is set.
          Since positive means MSB = 0 and negative means MSB = 1, this means you just need to check the MSB of the operands, and if needed, check the MSB of the result.
When subtracting 2 integers:
  subtracting is adding the 2’s complement, so calculate the 2’s complement of the source, then follow the rules for adding 2 integers.
What will be the values of the given flags after each operation?
0 0
1 0
1

## Slide 40: What's Next
Addition and subtraction
Status flags in addition and subtraction
Unsigned multiplication and division
Signed multiplication and division

## Slide 41: MUL Instruction
The MUL (unsigned multiply) instruction multiplies an 8-, 16-, or 32-bit operand by the value in AL, AX, or EAX.
MUL has only one input operand, the second input is part of the EAX register. Syntax:
    MUL r/m8 ; 8 bit register or memory
    MUL r/m16 ; 16 bit register or memory
    MUL r/m32 ; 32 bit register or memory
The size of the input operand dictates which part of the EAX register will be used as the multiplicand.
The product is always twice the size of the 2 operands, as shown:
Implied operands:

## Slide 42: MUL Examples
100h * 2000h, using 16-bit operands:
.data
val1 WORD 2000h
val2 WORD 100h
.code
mov ax,val1
mul val2 ; DX:AX = 00200000h, CF=1
CF indicates whether or not the upper half of the product contains significant digits.
mov eax,12345h
mov ebx,1000h
mul ebx ; EDX:EAX = 0000000012345000h, CF=0
12345h * 1000h, using 32-bit operands:

## Slide 43: Your turn . . .
mov ax,1234h
mov bx,100h
mul bx
What will be the hexadecimal values of DX, AX, and CF after the following instructions execute?
DX = 0012h, AX = 3400h, CF = 1

## Slide 44: Your turn . . .
mov eax,00128765h
mov ecx,10000h
mul ecx
What will be the hexadecimal values of EDX, EAX, and CF after the following instructions execute?
EDX = 00000012h, EAX = 87650000h, CF = 1

## Slide 45: DIV Instruction (1 of 2)
The DIV (unsigned divide) instruction performs 8-, 16-, and 32-bit division on unsigned integers.
One input operand is required (register or memory operand), which will be the divisor.
The dividend needs to be stored in AX, DX:AX, or EDX:EAX. The size of the input operand dictates whether it is 8-, 16-, or 32-bit division.
The dividend needs to be extended before calling the DIV instruction.
Example: To divide 100h by 10h, using 16-bit division:
    Store 100h (the dividend) into AX
    Extend the dividend by putting 0 into DX. Since DIV will use the DX:AX combination to do the division, we don’t want garbage data in DX.
    Store 10h (divisor) into CX (or any general purpose register other than dx and ax)
    Call DIV: div cx

## Slide 46: DIV Instruction (2 of 2)
The quotient and remainder will overwrite the dividend: the quotient will overwrite the lower half of the dividend, the remainder will overwrite the upper half of the dividend.
The quotient and remainder are always half the size of the dividend.
Instruction format
DIV r/m8 ; 8-bit register or memory argument
    DIV r/m16 ; 16-bit register or memory argument
    DIV r/m32 ; 32-bit register or memory argument
Implied Operands:

## Slide 47: DIV Examples
Divide 8003h by 100h, using 16-bit operands:
mov dx,0 ; clear dividend, high
mov ax,8003h ; dividend, low
mov cx,100h ; divisor
div cx ; AX = 0080h (quotient),
; DX = 3 (remainder)
Same division, using 32-bit operands:
mov edx,0 ; clear dividend, high
mov eax,8003h ; dividend, low
mov ecx,100h ; divisor
div ecx ; EAX = 00000080h, EDX = 3

## Slide 48: Your turn . . .
mov dx,0087h
mov ax,6000h
mov bx,100h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer. Divide overflow is when the quotient is a large value and cannot fit in the size register that is supposed to store it.
DX = 0000h, AX = 8760h

## Slide 49: Your turn . . .
mov dx,0087h
mov ax,6002h
mov bx,10h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer.
Divide Overflow

## Slide 50: What's Next
Addition and subtraction
Status flags in addition and subtraction
Unsigned multiplication and division
Signed multiplication and division

## Slide 51: IMUL Instruction
IMUL (signed integer multiply) multiplies an 8-, 16-, or 32-bit signed operand by either AL, AX, or EAX.
Similar to MUL, the size of the input argument dictates which part of EAX will be used, and the result is always twice the size of the input argument.
Unlike MUL, IMUL preserves the sign of the product by sign-extending it into the upper half of the destination register.
Example: multiply 48 * 4, using 8-bit operands:
mov al,48
mov bl,4
imul bl ; AX = 00C0h, OF=1
OF=1 because AH is not a sign extension of AL
OF indicates whether or not the sign bit has been extended for a negative result

## Slide 52: IMUL Examples
Multiply 4,823,424 * -423:
mov eax,4823424
mov ebx,-423
imul ebx ; EDX:EAX = FFFFFFFF86635D80h, OF=0
OF = 0 because EDX is a sign extension of EAX

## Slide 53: Your turn . . .
mov ax,8760h
mov bx,100h
imul bx
What will be the hexadecimal values of DX, AX, and OF after the following instructions execute?
DX:AX = FF876000h OF = 1 because DX is not a sign extension of AX

## Slide 54: Signed Integer Division
Since the dividend is always extended before a division, signed integers must be sign-extended before division takes place.
This is done by filling the high byte / word / doubleword with a copy of the low byte / word / doubleword's sign bit.
In the example below, 1000 1111 is the value to be divided, with a sign bit of 1. Before doing the division, the dividend needs to be sign extended and filled the upper half of the dividend.

## Slide 55: CBW, CWD, CDQ Instructions
The CBW, CWD, and CDQ instructions provide sign-extension operations:
  CBW (convert byte to word) sign extends AL into AH
  CWD (convert word to doubleword) sign extends AX into DX
  CDQ (convert doubleword to quadword) sign extends EAX into EDX
When doing signed division, do not extend the upper half of the dividend by zero-fill as with unsigned division. Instead, use the sign-extension instructions, which will fill with the sign bit correctly for you.
Example:
    mov eax,0FFFFFF9Bh ; (-101)
    cdq ; EDX:EAX = FFFFFFFFFFFFFF9Bh

## Slide 56: IDIV Instruction
IDIV (signed divide) performs signed integer division.
IDIV has the same syntax and operands as DIV instruction.
Remember to sign extend the dividend.
Example: 16-bit division of –48 by 5
mov ax,-48
cwd ; extend AX into DX
mov bx,5
idiv bx ; AX = -9, DX = -3
Example: 32-bit division of –48 by 5
mov eax,-48
cdq ; extend EAX into EDX
mov ebx,5
idiv ebx ; EAX = -9, EDX = -3

## Slide 57: Your turn . . .
mov ax,0FDFFh
cwd
mov bx,100h
idiv bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer.
DX = FFFFh (-1), AX = FFFEh (-2)

## Slide 58: Unsigned Arithmetic Expressions
Some good reasons to learn how to implement integer expressions:
  Learn how to optimize it.
  Test your understanding of NEG, INC, DEC, ADD, SUB, MUL, IMUL, DIV, IDIV.
  Check for overflow (Carry and Overflow flags).
Example: var4 = (var1 + var2) * var3
; Assume unsigned operands
mov eax,var1
add eax,var2 ; EAX = var1 + var2
mul var3 ; EAX = EAX * var3
; assume no overflow for now,
; we’ll check for overflow in a
; later chapter
mov var4,eax ; save product

## Slide 59: Signed Arithmetic Expressions (1 of 2)
Write assembly code for these arithmetic expressions, then compare your code with the solution below each expression.
Example: eax = (-var1 * var2) + var3
mov eax,var1
neg eax
imul var2
add eax,var3
Example: var4 = (var1 * 5) / (var2 – 3)
mov eax,var1 ; first do left side of division
mov ebx,5
imul ebx ; why can’t we do: imul 5 ?
mov ebx,var2 ; now for right side of division
sub ebx,3
idiv ebx ; EAX = quotient
mov var4,eax

## Slide 60: Signed Arithmetic Expressions (2 of 2)
Example: var4 = (var1 * -5) / (-var2 % var3);
mov eax,var2 ; first do right side of division
neg eax
cdq ; sign-extend dividend
idiv var3 ; EDX = remainder
mov ebx,edx ; EBX = right side of division
mov eax,-5 ; now for left side of division
imul var1 ; EDX:EAX = left side of division
idiv ebx ; final division
mov var4,eax ; quotient
To optimize the evaluation of an expression:
Try not to use memory variables, use registers instead.
Using the correct choice of registers can reduce the number of instructions because you don’t have to move data back and forth.
Sometime it's simplest to calculate the right-hand term of an expression first.

## Slide 61: More Examples
mov eax,20
imul ebx
idiv ecx
Implement the following expression using signed 32-bit integers:
eax = (ebx * 20) / ecx
Implement the following expression using signed 32-bit integers. Do not modify any variables other than var3:
var3 = (var1 * -var2) / (var3 – ebx)
mov eax,var1
mov edx,var2
neg edx
imul edx ; left side at EDX:EAX
mov ecx,var3
sub ecx,ebx
idiv ecx ; EAX = quotient
mov var3,eax

## Slide 62: Summary of Key Concepts
62
INC is shorter than ADD when incrementing by 1, DEC is shorter than SUB when decrementing by 1.
When adding and subtracting unsigned integers, check CF for invalid results.
When adding and subtracting signed integers, check OF for invalid results.
Use MUL and DIV for unsigned integers.
Use IMUL and IDIV for signed integers.
Before using DIV, zero out the upper half of the dividend in EDX / DX/ AH.
Before using IDIV, use the convert instructions to sign extend the upper half of the dividend in EDX / DX/ AH.
To optimize arithmetic expression evaluation, plan ahead the order of operations and keep data in the appropriate registers.